## Slide 1: Welding, Soldering & Brazing

## Slide 2: Welding
Defined as the metallurgical joining of two metal
pieces together to produce essentially a single
piece of metal.
Uses: Fabrication work - metal plates, rolled steel sections - castings of ferrous metals are joined together Repairing broken metal parts

## Slide 3
Classification
CARBON ARC
FUSION WELDING
PRESSURE WELDING
FORGE WELDING
RESISTANCE
WELDING
THERMITWELDING
ARC WELDING
GAS WELDING
SPOT WELDING
BUTT WELDING
SEAM WELDING
PERCUSSION WELDING
METAL ARC
ATOMIC HYDROGEN
WELDING

## Slide 4
Parts to be joined are heated to the molten state and allowed to
solidify
Parts to be joined are heated to plastic state then joined together
by applying external pressure
Pressure welding | Fusion Welding
Forge welding
Resistance welding
Arc welding
Gas welding
Non pressure welding

## Slide 5
Movable Jaw
Stationary Jaw
Welding gun
Metal parts
Resistance welding

## Slide 7
- Uses the principle of both the pressure & fusion welding
PRINCIPLE
- Consists of heating of the parts to be welded to the plastic
state and joined together by applying the mechanical pressure
- Parts are heated by passing a heavy electric current
- Current encounters very high resistance at the joints, as
a result temperature increases
- When temperature exceeds melting temperature of the
parts external mechanical pressure is applied
- Joining thin metal sheets and wires
Resistance welding

## Slide 8: Advantages:
Little pollution
Efficient energy use
High production rates
Disadvantages:
Used for joining relatively thin materials
Equipment is costly

## Slide 9
Clamp
Figure : Principle of Arc welding
Cables
Electrode holder
Electrode
Arc
Power source
(AC / DC)
Workpiece
Principle of Electric Arc welding

## Slide 15
Principle:
Plates before welding
Welded joint
Slag
Plates to be welded will act as one pole of the electric circuit
Electrode held by the operator forms the other pole
When electrode comes in contact with the plates arc is formed
Intense heat melts the edges of 2 plates & creates a molten
metal pool
Electrode tip neat the arc also melts & enters the pool
Strong joint is formed when molten metal cools & solidifies

## Slide 16
Types of welding electrodes
WELDING ELECTRODES
Consumable electrodes
Non-consumable electrodes
Bare
Coated
Melts along with the workpieces and fills the joint.
Consumable electrodes
Non-consumable electrodes
Requires additional filler material
Amount of the metal deposited by the filler rod can be controlled
Advantage:

## Slide 17
1) Bare 2) Lightly coated 3) Coated a) FLUX b) WIRE
Coated and non-coated electrodes
a
b

## Slide 19
- Protection of molten metal from oxygen and nitrogen of
the air by providing a gas shield around the arc and
the molten pool of metal
- Establish and maintain the arc throughout welding
- formation of slag over the joint thus protects from rapid
cooling
Functions of a coated electrode
Limitation of a bare electrode
- Non metallic constituents gets trapped in the solidifying
Weld metal
- Reduces the strength of the joint

## Slide 23
GAS WELDING

## Slide 24
Gas welding flames
Oxidizing flame
Carburizing flame
Neutral flame

## Slide 28
Gas welding flames

## Slide 29
Gas Flames
Oxidizing flame
Carburizing flame
Neutral flame
Obtained by supplying equal volumes of oxygen & acetylene
Used in oxy-acetylene welding
Obtained by supplying excess acetylene in the gas ratio 0.95 to 1
Consists of 2 cones
used in welding of alloy steels, cast iron & aluminium
Obtained by supplying excess oxygen in the gas ratio 1.15 to 1.5
Inner white cone is shorter
Not suitable for welding

## Slide 30
Molten weld metal
Torch Tip
Inner cone
Welding rod
Solidified weld metal
Base metal
Direction of welding
Oxy-Acetylene gas welding

## Slide 31
Principle:
Fusion method of welding
Strong gas flame is used to raise the temperature of the
work pieces to melt their edges
Filler metal is used to fill the joint
Oxygen – Acetylene mixture is most commonly used
in gas welding

## Slide 32
SOLDERING & BRAZING
Filler metal: brass or solder
Base metal
Characteristics of a brazed or soldered joint

## Slide 33
A method of uniting two thin metal pieces using a
dissimilar metal or an alloy by the application of heat
SOLDERING
BRAZING
A method of joining two similar or dissimilar metals using a special fusible alloy

## Slide 34
Clean the joint surfaces & to prevent oxidation
Zinc Chloride
Flux
Soft solder
  Alloy of lead and tin
  Melting temperature, 150 – 3500C
Hard solder
  Alloy of copper , tin and silver
  Soldering temperature, 600 – 9000C
  Used for stronger joints
SOLDERING

## Slide 35
Brazing | Soldering
Less stronger joints
Does not yield a good surface finish
Melting point of the filler material is above 4500C
Melting point of the filler material is below 4500C
Only similar metals can be joined
Dissimilar metals can be joined easily
Good surface finish
Stronger joints
Distinguish between brazing and soldering

## Slide 36
Soldering, Brazing | Welding
Comparison of Soldering, brazing and welding
No direct melting of the base metals being joined
Direct melting of the base metals being joined
Useful for joining similar & dissimilar metals
Useful for joining similar metals
Filler materials are solder and brazing alloy
Brazing alloy and the solder have low melting points than the metals to be joined
Welding alloy has high melting point than the metals to be joined
Welding rod is used as filler material

## Slide 37
WELD DEFECTS
Cracking
  Due to incorrect electrodes / wrong procedure
  Remedy: Re-welding
Incorrect Edge preparation
  Too Narrow angle between edges result in weak weld
  Tool wide angle between edges results in overheating
Craters
  Concave depressions in the external surface of the joint
Under-cutting
  Excess melting of parent metal which reduces its strength
Porous weld
  Insufficient gap between electrode & workpiece results in poor penetration
Over welding

## Slide 38
WELD DEFECTS
Cracking
  Due to incorrect electrodes / wrong procedure
  Remedy: Re-welding
Incorrect Edge preparation
  Too Narrow angle between edges result in weak weld
  Tool wide angle between edges results in overheating
Craters
  Concave depressions in the external surface of the joint
Under-cutting
  Excess melting of parent metal which reduces its strength
Porous weld
  Insufficient gap between electrode & workpiece results in poor penetration
Over welding
  Welding carried over an already welded layer
  Results in over heating the earlier layer

## Slide 44: Joint types
Butt
Tee
Lap
Corner
Edge