## Slide 1
Smithing & Forging

## Slide 2
Smithing
It is a process of performing various operations on relatively small work pieces, heated in an open fire (hearth) by means of hand hammers or small power hammers in a smithy shop.
Forging
Is a process of producing those parts, which must be heated in a closed furnace, by means of heavy hammers or forging machines or presses.

## Slide 3
2) Fuller
4) Flatter
5) Swage
6) Flat tongs
7) Ring Tongs
8) Gad Tongs
Forging Tools
Beak
9) Swage block
3) Punch

## Slide 4
Set Hammer
a) Ball peen
b) Cross peen
c) Straight peen
Sledge Hammer
Hammers
Chisels
Hot Chisel
Set hammer

## Slide 5
Anvil: Provides a support for blacksmith’s workpiece when hammering.
-Beak is used for bending the workpieces
Fuller: Necking down a piece of work
Swage: To obtain reduced and finished to round, square or hexagonal form
- Made with half grooves of dimensions to suit the work being reduced
Punch: Used for making holes in metal part when it is in forging heat.
Flatter: To give smoothness and accuracy to components which have been already shaped by fullers and swages.

## Slide 6
Back
ANVIL

## Slide 7
SWAGE BLOCK

## Slide 9
Tongs: To hold the workpiece
Flat Tong : For holding work of rectangular section
Ring Tong : For holding work of circular section
Gad Tong : For general pick-up, either straight or tapered
Swage block:
Used for squaring, sizing, bending operations
Chisels: For cutting metals & for nicking prior to breaking
- They may be hot or cold depending on the metal to be cut
is hot or cold.
Hand hammers: They may be classified as a) Ball peen hammer
b) Straight peen hammer c) Cross peen hammer
d) Sledge hammer
Set hammer: Used for finishing corners in shouldered work, where flatter is inconvenient.

## Slide 10
Forging processes
Smith Die forging
    a) Hand Forging
    b) Power Forging
They are classified as:
2) Impression Die forging
    a) Drop Forging
    b) Press Forging
    c) Machine Forging

## Slide 11
Power forging
Work
Ram
Anvil
Upper Die
Lower Die
Fig. Steam Hammer
-Also called as an air and
steam hammer
-Operated by either steam or
compressed air
Principle of operation is
illustrated in the sketch
Require additional facilities
for supplying high pressure steam or compressed air.

## Slide 12
work
Lower Die
Upper Die
Roll
Board
Drop Forging (Stamping/ Die forging)
Fig. Board Hammer
Also called as Gravity Hammer
Working:
Ram is fixed to the lower end of
the board
Board is placed between 2 rolls
Ram will be lifted, when both rolls
are pressed against the board
-Working stroke is produced when
the rolls are released.
-Process continues till operator
holds down the treadle

## Slide 13
Smith forging operations
Most commonly used forging operations are:
  Upsetting
  Bending
  Punching
  Drawing down
  Setting down
  Cutting
  Fullering

## Slide 14
Smith forging operations
Upset forging operations
Curvilinear
Angular
Bending operations
Upsetting:
Process of increasing the thickness of a bar by reducing its length by end pressure.
Bending:
Process of producing curvilinear or angular bends on a bar.
Done on the edge of the anvil face or beak or swage block

## Slide 15
Step 1
Step 2
Step 3
Punching operation
Process of producing of holes by a hot punch by placing the job over the pritchel hole of the anvil.

## Slide 16
Drawing down or Swaging
Process of increasing the length of a bar at the expense of its width or thickness or both.
Setting Down
It is a localized drawing down or swaging operation.
Process of spreading the metal along the length of the job.
Fullering
Cutting
Process of removing a forging from the stock.

## Slide 17
Drop forging
Uses drop hammers of 2 types
Hammers can make 50 – 75 strokes/ min
Lower maintenance cost & easy to operate
Tools, Gear blanks, Machine parts
Gravity hammer
Steam hammer
Press forging
Done in presses than with hammers
More accurate than drop forgings
Relatively slow squeezing but better penetration
Screws, nuts & rivets can be made
High operating speed

## Slide 18
Machine / Upset forging
Lengthwise pressure will be applied on the component held
between grooved dies to enlarge some sections
Operates at very high rate
Bolts, nuts, washers can be made
Produce 400 – 600 forgings per hour